## Slide 1
Gururaj Saileshwar
Bolin Wang, Moinuddin Qureshi, Prashant Nair
Randomized Row-Swap: Mitigating Row Hammer By Breaking Spatial Correlation Between Aggressor and Victim Rows

## Slide 2: Rowhammer Attacks on DRAM
DRAM Scaling for Increased Capacity
DRAM
(old)
DRAM
(new)
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 3: Rowhammer Attacks on DRAM
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)

## Slide 4: Rowhammer Attacks on DRAM
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
Row
Row
Row
Row of Cells (8KB)
DRAM

## Slide 5: Rowhammer Attacks on DRAM
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
8 Byte
Row
Row
Row
Row of Cells (8KB)
DRAM

## Slide 6: Rowhammer Attacks on DRAM
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
8 Byte
Refresh
Every 64ms
Row
Row
Row
Row of Cells (8KB)
DRAM

## Slide 7: Rowhammer Attacks on DRAM
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
DRAM
Rowhammer Attack
[Kim+, ISCA’15]
Rapid
Accesses
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 8: Rowhammer Attacks on DRAM
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
Victim Row
Aggressor Row
Aggressor Row
DRAM
Rowhammer Attack
[Kim+, ISCA’15]
Rapid
Accesses
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)

## Slide 9: Rowhammer Attacks on DRAM
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
Victim Row
Aggressor Row
Aggressor Row
DRAM
Rowhammer Attack
[Kim+, ISCA’15]
Rapid
Accesses
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Software Adversary Can Flip Bits in Page Tables &
Gain Kernel Privileges (Take Over a System)
[Seaborn+, Blackhat’15]
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 10
Notes: Even the folks at Netflix seem to know about Rowhammer and are using it as a plot construct in of their TV Shows.

## Slide 11: Mitigation in Commercial DDR4
Victim Row
Aggressor Row
Victim Row
DRAM
Targeted Row Refresh (TRR) in DDR4 (2015)

## Slide 12: Mitigation in Commercial DDR4
Track Aggressor Rows
1
Victim Row
Aggressor Row
Victim Row
DRAM
Targeted Row Refresh (TRR) in DDR4 (2015)

## Slide 13: Mitigation in Commercial DDR4
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Targeted Row Refresh (TRR) in DDR4 (2015)

## Slide 14
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
TRResspass Breaks TRR Tracker [Frigo+, SP’20]
Source: The Hacker News
Blacksmith Attack: All DRAM Shown Vulnerable [Jattke+, SP’22]
Source: The Register
Mitigation in Commercial DDR4: Broken!
Targeted Row Refresh (TRR) in DDR4 (2015)

## Slide 15: Recent Victim Focused Mitigations
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Principled Tracking
Graphene [MICRO’20]
TWICE [ISCA’19]
CRA [CAL’14]
and others …

## Slide 16: Recent Victim Focused Mitigations
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh

## Slide 17: Recent Victim Focused Mitigations
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Google’s Half-Double Attack:
Exploits Mitigative Refresh [2021]
Source: ArsTechnica
Track Aggressor Rows
1
Mitigative Action
2

## Slide 18: Recent Victim Focused Mitigations
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Distance-2
Distance-2
Track Aggressor Rows
1
Mitigative Action
2
Google’s Half-Double Attack:
Exploits Mitigative Refresh [2021]
Source: ArsTechnica

## Slide 19: Recent Victim Focused Mitigations
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Distance-2
Distance-2
Need New Mitigative Action Resilient to Current and Emerging Attack Patterns
(preferably without requiring knowledge of DRAM mapping function)
Track Aggressor Rows
1
Mitigative Action
2
Google’s Half-Double Attack:
Exploits Mitigative Refresh [2021]
Source: ArsTechnica

## Slide 20: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
Aggressor
.
.
Row-X
Notes: To mitigate Rowhammer in a future proof manner, we focus on a new mitigative action that aggressor-focused (not victims).
The key idea is to track aggressor rows and remap them to break the spatial correlation between agressors and victims.
So the key idea of Row-Swap is to break the spatial co-relation between aggressor rows and victim rows pre-emptively. If a row crosses T = TRH/k, we simply swap it with a randomly selected row in same bank of the DRAM.
Now the aggressor row is mapped to some other random row, and a random virtual address is mapped to the row that is already attacked. Because there are 100s of thousands of rows in a DRAM and adversary can attack at most 1.36 / 800 rows and cause 1700 rows to swap, it is not easy for the adversary to identify rows that have already been swapped. And even if it does, the row would be swapped again after T activations.
With this design, we provide the guarantee that no row can be activated more than TRH times, With a TRH of 4.8K, that is lower than all known attacks (single-sided, double-sided, half-double), we can prevent all known attacks in a principled manner.

## Slide 21: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
.
.
Row-X
Aggressor
Notes: To mitigate Rowhammer in a future proof manner, we focus on a new mitigative action that aggressor-focused (not victims).
The key idea is to track aggressor rows and remap them to break the spatial correlation between agressors and victims.
So the key idea of Row-Swap is to break the spatial co-relation between aggressor rows and victim rows pre-emptively. If a row crosses T = TRH/k, we simply swap it with a randomly selected row in same bank of the DRAM.
Now the aggressor row is mapped to some other random row, and a random virtual address is mapped to the row that is already attacked. Because there are 100s of thousands of rows in a DRAM and adversary can attack at most 1.36 / 800 rows and cause 1700 rows to swap, it is not easy for the adversary to identify rows that have already been swapped. And even if it does, the row would be swapped again after T activations.
With this design, we provide the guarantee that no row can be activated more than TRH times, With a TRH of 4.8K, that is lower than all known attacks (single-sided, double-sided, half-double), we can prevent all known attacks in a principled manner.

## Slide 22: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
Row
Swap
Random
.
.
T activations
Aggressor
Row-X

## Slide 23: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
.
.
Aggressor
Row-X
Row-Y

## Slide 24: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
.
.
Row-X
Row
Swap
Random
T activations
Row-Y
Aggressor

## Slide 25: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
.
.
Row-X
Row-Y
Aggressor
Security Guarantee: No Row Crosses Rowhammer Threshold Activations within 64ms
Refresh
Every 64ms

## Slide 26: Aggressor Focused Mitigation: Randomized Row-Swap
Key Idea: Remap Aggressor Rows to Break Spatial Correlation with Victim Rows
Victim
Victim
.
.
Row-X
Row-Y
Aggressor
Security Guarantee: No Row Crosses Rowhammer Threshold Activations within 64ms
Refresh
Every 64ms
Lower T (Swap Threshold)  Better Security

## Slide 27: Security Analysis
TRH=4800  Minimum Activations in 64ms on Row for Rowhammer via Any Pattern (Single-sided, Double-Sided, Half-Double)
Notes: To mitigate Rowhammer in a future proof manner, we focus on a new mitigative action that aggressor-focused (not victims).
The key idea is to track aggressor rows and remap them to break the spatial correlation between agressors and victims.
So the key idea of Row-Swap is to break the spatial co-relation between aggressor rows and victim rows pre-emptively. If a row crosses T = TRH/k, we simply swap it with a randomly selected row in same bank of the DRAM.
Now the aggressor row is mapped to some other random row, and a random virtual address is mapped to the row that is already attacked. Because there are 100s of thousands of rows in a DRAM and adversary can attack at most 1.36 / 800 rows and cause 1700 rows to swap, it is not easy for the adversary to identify rows that have already been swapped. And even if it does, the row would be swapped again after T activations.
With this design, we provide the guarantee that no row can be activated more than TRH times, With a TRH of 4.8K, that is lower than all known attacks (single-sided, double-sided, half-double), we can prevent all known attacks in a principled manner.

## Slide 28: Security Analysis
TRH=4800  Minimum Activations in 64ms on Row for Rowhammer via Any Pattern (Single-sided, Double-Sided, Half-Double)
Victim
Victim
Row
Swap
Random
.
.
T activations
Aggressor
Row-X

## Slide 29: Security Analysis
TRH=4800  Minimum Activations in 64ms on Row for Rowhammer via Any Pattern (Single-sided, Double-Sided, Half-Double)
Victim
Victim
Row
Swap
Random
.
.
T activations
Aggressor
Row-X
Random
Guess?

## Slide 30: Security Analysis
TRH=4800  Minimum Activations in 64ms on Row for Rowhammer via Any Pattern (Single-sided, Double-Sided, Half-Double)
Victim
Victim
Row
Swap
Random
.
.
T activations
Aggressor
Row-X
Random
Swaps in 64 ms
Rows in a
DRAM Bank
(128K)
Balls
Buckets
Buckets and Balls Problem
Random
Guess?

## Slide 31: Security Analysis
TRH=4800  Minimum Activations in 64ms on Row for Rowhammer via Any Pattern (Single-sided, Double-Sided, Half-Double)
Victim
Victim
Row
Swap
Random
.
.
T activations
Aggressor
Row-X
Random
Swaps in 64 ms
Rows in a
DRAM Bank
(128K)
Balls
Buckets
Buckets and Balls Problem
Swap Every T Activations | Attack Time
T = TRH/5 | 6.9 days
T = TRH/6 | 3.8 years
T = TRH/7 | 762 years
Random
Guess?

## Slide 32: Security Analysis
TRH=4800  Minimum Activations in 64ms on Row for Rowhammer via Any Pattern (Single-sided, Double-Sided, Half-Double)
Victim
Victim
Row
Swap
Random
.
.
T activations
Aggressor
Row-X
Random
Swaps in 64 ms
Rows in a
DRAM Bank
(128K)
Balls
Buckets
Buckets and Balls Problem
Swap Every T Activations | Attack Time
T = TRH/5 | 6.9 days
T = TRH/6 | 3.8 years
T = TRH/7 | 762 years
Continuous Remapping of Aggressor Rows Provides Principled Security for Years of Attack
Random
Guess?

## Slide 33: Implementation of Randomized Row Swap
DRAM Access
Hot Row Tracker (HRT)
[Graphene, MICRO’20]
Row Indirection Table (RIT)
Swapped
Not Swapped
Row
Row
Row
Row
DRAM
Row
Row
Row
Memory Controller
RRS Structures
Notes: We manage the swap structure with a indirection table, and similarly have a tracking structure using the Misra-Gries algorithm similar to Graphene. We design scalable structures for these in the paper. Take a look in the paper.

## Slide 34: Collision Avoidance Table (CAT) for RIT and HRT
Problem: The tracking structures can be overwhelmed by repeated accesses
A
B
C
D
Sets
Ways

## Slide 35: Collision Avoidance Table (CAT) for RIT and HRT
Problem: The tracking structures can be overwhelmed by repeated accesses
A
B
C
D
E
Sets
Ways

## Slide 36: Collision Avoidance Table (CAT) for RIT and HRT
Problem: The tracking structures can be overwhelmed by repeated accesses
A
Conflicts in tracking structures  targeted row addresses to be expelled  Lose tracking of some rows
E
B
C
D

## Slide 37: Collision Avoidance Table (CAT) for RIT and HRT
Solution: Leverage Power of Two Choices [MIRAGE – USENIX SEC’21]
Additional Ways + Multiple Hashes + Load Balancing + Random Replacement
U
V
W
X
A
B
C
D
hash1
hash2
E

## Slide 38: Collision Avoidance Table (CAT) for RIT and HRT
Solution: Leverage Power of Two Choices [MIRAGE – USENIX SEC’21]
Additional Ways + Multiple Hashes + Load Balancing + Random Replacement
U
V
W
X
A
B
C
D
hash1
hash2
E

## Slide 39: Collision Avoidance Table (CAT) for RIT and HRT
Solution: Leverage Power of Two Choices [MIRAGE – USENIX SEC’21]
Additional Ways + Multiple Hashes + Load Balancing + Random Replacement
U
V
W
X
A
B
C
D
hash1
hash2
E
RIT and HRT use the CAT to avoid collisions  Prevents Conflict-Based Attacks

## Slide 40: Collision Avoidance Table (CAT) for RIT and HRT
Solution: Leverage Power of Two Choices [MIRAGE – USENIX SEC’21]

## Slide 41: Collision Avoidance Table (CAT) for RIT and HRT
Solution: Leverage Power of Two Choices [MIRAGE – USENIX SEC’21]
With 14 Demand Ways and 6 Extra Ways  1030 installs are needed to create a conflict

## Slide 42: Implementation of Randomized Row Swap
DRAM Access
Hot Row Tracker (HRT)
[Graphene, MICRO’20]
Row Indirection Table (RIT)
Swapped
Not Swapped
Row
Row
Row
Row
DRAM
Row
Row
Row
Memory Controller
RRS Structures
Notes: We manage the swap structure with a indirection table, and similarly have a tracking structure using the Misra-Gries algorithm similar to Graphene. We design scalable structures for these in the paper. Take a look in the paper.

## Slide 43: Implementation of Randomized Row Swap
DRAM Access
Hot Row Tracker (HRT)
[Graphene, MICRO’20]
Row Indirection Table (RIT)
Swapped
Not Swapped
Row
Row
Row
Row
DRAM
Row
Row
Row
Memory Controller
RRS Structures
SRAM Storage Overheads (RIT, HRT)  45 KB Per DRAM Bank x 16 Banks  720 KB of SRAM

## Slide 44: Performance Impact of Row Swaps
Frequency of Row Swaps Per 64ms
(1.5 microseconds per swap)
Chart: Number of Row Swaps (64ms)
| SPEC2K6(29) | SPEC2K17(22) | GAP(6) | COMM(5) | PARSEC(7) | BIOBENCH(2) | MIX(6) | ALL(78)
Column2 | 151.02 | 10.156 | 1.876 | 22.296 | 26.131 | 73.204 | 37.369 | 67.683
< 100 Swaps Per 64ms
Notes: Overall, in terms of performance, the impact is negligible primarily because the frequency of swaps is negligible.
Storage overhead is modest ~40KB per memory bank (16 banks in DDR4).

## Slide 45: Performance Impact of Row Swaps
Frequency of Row Swaps Per 64ms
(1.5 microseconds per swap)
Negligible Performance Impact
(0.4% slowdown on average)
Chart: Normalized Performance
| SPEC2K6(29) | SPEC2K17(22) | GAP(6) | COMM(5) | PARSEC(7) | BIOBENCH(2) | MIX(6) | ALL(78)
Column2 | 0.993 | 0.998 | 1 | 0.997 | 0.997 | 0.995 | 0.997 | 0.996
Chart: Number of Row Swaps (64ms)
| SPEC2K6(29) | SPEC2K17(22) | GAP(6) | COMM(5) | PARSEC(7) | BIOBENCH(2) | MIX(6) | ALL(78)
Column2 | 151.02 | 10.156 | 1.876 | 22.296 | 26.131 | 73.204 | 37.369 | 67.683
< 100 Swaps Per 64ms

## Slide 46: Performance Impact of Row Swaps
Frequency of Row Swaps Per 64ms
(1.5 microseconds per swap)
Negligible Performance Impact
(0.4% slowdown on average)
Saileshwar et al. Randomized Row-Swap: Mitigating Row Hammer by Breaking Spatial Correlation. In ASPLOS 2022
Randomized Row Swap has negligible performance impact due to infrequent swaps
Chart: Normalized Performance
| SPEC2K6(29) | SPEC2K17(22) | GAP(6) | COMM(5) | PARSEC(7) | BIOBENCH(2) | MIX(6) | ALL(78)
Column2 | 0.993 | 0.998 | 1 | 0.997 | 0.997 | 0.995 | 0.997 | 0.996
Chart: Number of Row Swaps (64ms)
| SPEC2K6(29) | SPEC2K17(22) | GAP(6) | COMM(5) | PARSEC(7) | BIOBENCH(2) | MIX(6) | ALL(78)
Column2 | 151.02 | 10.156 | 1.876 | 22.296 | 26.131 | 73.204 | 37.369 | 67.683
< 100 Swaps Per 64ms

## Slide 47: Comparison with Prior Aggressor Focused Mitigation
Blockhammer [HPCA’21]
Rate-Throttles Aggressors at Blacklist Point (Earlier Than RTH) For Entire 64ms

## Slide 48: Comparison with Prior Aggressor Focused Mitigation
Blockhammer [HPCA’21]
Rate-Throttles Aggressors at Blacklist Point (Earlier Than RTH) For Entire 64ms
Randomized Row Swap Incurs Much Lower Worst-Case Slowdowns vs Blockhammer
(mitigation is less expensive and hence adds less overheads in benign workloads)

## Slide 49: Takeways from Randomized Row Swap
New Aggressor-Focused Mitigation – Swaps Aggressors with Random Destinations & Successively Remaps --> No Row Crosses Rowhammer Threshold
Resilient to TRResspass [SP’20], Half-Double (2021), Blacksmith [SP’22] attacks
& potentially future attacks?
Row
Swap
Randomized Row Swap incurs modest costs (0.4% slowdown, ~40KB SRAM/bank) while providing security against years of continuous attack

## Slide 50: Thank You
Gururaj Saileshwar
Assistant Professor